## Slide 1
Retrofitting Businesses and Industries for the Bay TMDL
KC Filippino, Hampton Roads Planning District Commission & Mike Barbachem, Hazen & Sawyer
Work funded by the National Fish and Wildlife Foundation (NFWF) , Chesapeake Bay Small Watershed Planning Grant

## Slide 2
Part 1: Background & Purpose
01
Hampton Roads & what makes up our Bay loads
02
Phase III WIP commitments
Part 2: Methods
04
Mapping exercise
05
Scoring and ranking
06
Communication
Part 3: Findings
07
Industrial partners
08
BMPs and incentives
09
More work to be done
Outline
03
Unregulated vs regulated

## Slide 3
1 of 22 Planning District Commissions in VA
17 localities, 15 in the Bay watershed
6 Phase I and 5 Phase II MS4 permittees, many non-traditional permittees
3 Soil Water Conservation Districts
1 regional wastewater entity
Several federal facilities
Multiple environmental NGOs
Support from consultants and academics
Regional Collaboration

## Slide 4
What makes up Bay loads in Hampton Roads?
Nitrogen & Phosphorus contributions as of 2020
Natural lands = forest, wetlands, buffers:
10% TN; 27% TP
Wastewater & Septic:
55% TN; 42% TP
Agriculture:
8% TN; 2% TP
Regulated Developed
18% TN; 19% TP
Unregulated Developed
10% TN; 9% TP
For the Developed sector only, Unregulated Developed
accounts for:
40% of the acreage
35% of the developed TN load
33% of the developed TP load
How will those reductions be achieved?

## Slide 5
Bay TMDL success dependent upon voluntary and mandatory reductions
In Hampton Roads, wastewater and regulated stormwater are responsible for regulated reductions
40% of the developed land in the region is unregulated
Purpose: Address Phase III WIP needs
The Phase III WIP called on unregulated developed to make voluntary reductions
HRPDC applied for NFWF funding to find willing partners and explore options for BMP implementation and reporting

## Slide 6
Regulated for discharge through VA Pollution Discharge Elimination System (VPDES) permits
Bay TMDL requirements are for monitoring only
Many have stormwater runoff directly to waterways outside of any MS4 system
Many are part of existing stewardship programs and already doing great things
Industry partners

## Slide 7
1) Map industrial partners using VPDES permit information, floodplain boundaries, shoreline location, stewardship participation
2) Rank potential partners
3) Engage partners and develop plans
Methods

## Slide 8
Does it flood? Are they stewards already? Do they have shorelines that drain directly to local waters?
Scoring Matrix

## Slide 9
Lots of Opportunities
Locality | Heat Map Categories & # of parcels |  |  |  |  | 
 | 0, 0.5, 1.a, 1.b | 1.5, 2.a, 2.b | 2.5, 3.a, 3.b | 3.5, 4.a, 4.b | 4.5, 5.a, 5.b | 5.5, 6
Chesapeake | 2,261 | 356 | 2 |  | 99 | 7
Franklin | 204 | 294 |  |  |  | 
Gloucester County | 228 | 18 |  |  | 2 | 
Hampton | 1,501 | 374 | 3 |  | 375 | 2
Isle of Wight County | 77 | 69 | 1 |  | 6 | 
James City County | 1,914 | 18 |  |  | 9 | 1
Newport News | 2,210 | 140 |  |  | 22 | 1
Norfolk | 4,143 | 1,288 | 4 |  | 173 | 9
Poquoson | 5 | 25 |  |  | 6 | 
Portsmouth | 1,510 | 444 | 1 |  | 44 | 1
Smithfield | 19 | 2 |  |  | 4 | 1
Southampton County | 168 | 29 |  |  |  | 
Suffolk | 1,439 | 85 |  |  | 33 | 
Virginia Beach | 2,975 | 459 | 6 |  | 87 | 3
Williamsburg | 276 | 1 |  |  |  | 
Windsor | 20 | 6 |  |  |  | 
York County | 1,013 | 35 | 1 |  | 33 | 2
Total | 19,963 | 3,643 | 18 | 0 | 893 | 27

## Slide 10
What are you already doing? Interested in more? Care to report?
- Conduct email questionnaire
- Cold-calls
- Site visit
Survey partners

## Slide 11
Findings
Large pool of potential partners
BMPs and incentives
More work to be done

## Slide 12
20%
Reached 5 out of 27 industrial partners that ranked high
Potential to impact thousands of acres
Large pool of potential partners

## Slide 13
No problem with reporting existing BMPS - which aren't for Bay TMDL compliance - and implementing new ones for multiple benefits
Land Cover Practices preferred
  Living shorelines
  Pond retrofits
  Conservation landscaping
  Impervious pavement removal
Maintenance is key
  Verify through windshield surveys
BMPs can be implemented & reported

## Slide 14
Incentives Identified
BEING PART OF A STEWARDSHIP OPPORTUNITY & TEAM BUILDING
ACHIEVING COMPLIANCE FOR OTHER ISSUES & ADDRESSING FLOOD CONCERNS
FEE REDUCTIONS AND MORE FUNDING SOURCES

## Slide 15
Only had detailed conversations with 5 partners
Need to cast a wider net and develop contact lists
Incentives and achieving multiple benefits are keys to success
Potential for pilot implementation projects and partnerships
More work to be done

## Slide 16
Proposing Pilot
Implement BMPs for Bay TMDL and stewardship benefits
Report, track, and verify BMPs
Grow a coalition of the willing

## Slide 17
Stay Tuned...
KC Filippino, kfilippino@hrpdcva.gov